## Slide 1
What is the Application All About?
Permit to Work (PTW) Core Purpose & Authorized Personnel
PTW = Permission + Hazard Identification + Safety Controls + Sign-Off
Official formal authorization required before carrying out any hazardous job in an operational facility.
PERMIT RECEIVER
Field Supervisor
• Requests permit with JSA
• Briefs field work crew
• Stays at site continuously
PERMIT ISSUER
Area Custodian
• Verifies site isolation
• Tests gas levels & limits
• Authorizes safe start
PTW COORDINATOR
Operations Lead
• Registers all active jobs
• Prevents site conflicts
• Tracks 24-hr logbook
EHS OFFICER
Safety Advisor
• Audits critical safety controls
• Endorses high-risk permits
• Performs random spot checks
Features of this Application
Color-coded classifications, mandatory safety attachments, and strict time limits
Color-Coded Permits
Visual identification in the field
• RED: Hot Work (Welding, sparks, flame)
• BLUE: Cold Work (Hand tools, unbolting)
• GREEN: Confined Space Entry (Tanks, pits)
• ORANGE: Electrical & Lock-Out / Tag-Out
• PURPLE: Working at Height (> 1.8m)
• BROWN: Excavation & Trenching
Mandatory Attachments
Enforced pre-job documents
• JSA: Step-by-step hazard checklist
• Gas Test: O2 (19.5-23.5%), LEL (0%), H2S (0)
• Toolbox Talk: Daily briefing & crew sign-off
• P&ID Drawing: Marked mechanical spade blinds
• Rescue Plan: Standby personnel & rescue tripod
Validity & Audit Rules
Time boundaries & governance
• Single Shift: Valid 8 to 12 hours only
• Daily Revalidation: Joint morning check
• Maximum Lifetime: 6 days before renewal
• Worksite Display: Placed in field permit box
• Audit Trail: Permanent regulatory storage
Why is this Application Required?
Crucial risk reduction, life protection, and compliance enforcement
Accident & Explosion Prevention
Catastrophic Risk Control
• Stops uncontrolled ignition of hydrocarbons & explosive vapors
• Protects technicians from deadly toxic gases (H2S & CO)
• Guarantees safe atmospheric levels before any confined entry
Zero-Energy Isolation (LOTO)
Guaranteed Physical Protection
• Positive mechanical isolation via physical spade blind insertion
• Electrical Lock-Out & Tag-Out with personal locks and keys
• Prevents accidental equipment energization or valve openings
Conflict & SIMOPS Elimination
Cross-Crew Separation
• Prevents hot sparks falling onto lower-deck chemical operations
• Maintains critical physical safety barriers between contractors
• Gives the control room real-time visibility over all plant jobs
Legal Accountability & Compliance
Regulatory Defense
• Signed mutual agreement between operations and maintenance
• Every worker acknowledges hazards before touching equipment
• Provides an unalterable audit log for government & safety audits
How Does the Application Flow End-to-End?
Operational stages from initial job request to final closeout and archival
Stage 1
Submit Request
Receiver fills permit form and attaches Job Safety Analysis (JSA).
Stage 2
Technical Review
Issuer inspects site, applies LOTO locks, and logs blind tags.
Stage 3
Clash & Gas Check
PTW Coordinator resolves SIMOPS; gas tester certifies atmosphere.
Stage 4
Briefing & Display
Hold Toolbox Talk (TBT), sign attendance, display in field box.
Stage 5
Execution & Monitor
Active work commences under designated supervisor & standby watch.
Stage 6
Housekeeping & Close
Site cleaned, de-isolation verified, signatures logged, archived.
What Happens When Safety Incidents Occur?
Protocol for Simultaneous Operations (SIMOPS) and emergency incident response
SIMOPS (Simultaneous Operations)
Cross-Job Physical Clashes
• Vertical Conflicts: Hot sparks falling above fuel lines or lower crew
• Shared Utilities: Dual operations connecting to the same purge line
• Crane Overflights: Lifting heavy loads over active hydrocarbon piping
• Resolution Rule: Mandatory SIMOPS checklist & scheduled shift separation
Emergency Incident Protocol
Immediate Stop & Evacuation
• Stop Work Authority (SWA): Any worker has the right to halt work instantly
• Alarm Activation: Sirens sound -> equipment shut down, crew musters
• Automatic Invalidation: All active permits in the area voided immediately
• Mandatory Reset: Root cause fixed, fresh gas test & new permit issued